Uriae Walker
CS 410
Project 2
Moving Object Detection and Tracking

For this project the Android Java Camera was used to detect moving objects in viewing range of the Android phone camera.
Different approaches could have been taken in accomplishing this task of detection and tracking. My approach was to isolate the foreground (i.e) moving objects with in each frame by comparing the current frame with a previous frame to detect moving objects. Then, by repeating this method of detection for every frame and drawing bounding boxes around the isolated foreground objects I was able to effective track their movements across frames.
The algorithm for my approach proceeded as follows. First, I captured camera frames using the Android java camera callback onCameraFrame(). Once inside this function I preformed the necessary manipulations on the captured frame to facilitate detection and tracking. The first manipulation was done through the backgroundMOG function apply. apply takes a openCV Mat (image) and a learning rate and returns a foreground mask. By setting the learning rate to .1, I was about to produce desirable foreground masks that isolated the moving objects. After extracting the foreground mask I applied the OpenCV functions erode and dilate. Erosion takes the minimum value in a neighboring set of pixels, and dilation takes the maximum values in a set of pixels. Erosion and dilation techniques can help to remove noise and fill unwanted “holes” with in the image (holes could be things like space between a persons arm and body). A key parameter of the erode and dilate functions is ksize. This parameter defines the size of a pixel's “structuring element” (neighboring pixels), and in doing so can manipulate the extend of erosion or dilation. Next, we use the OpenCv function findContours this function finds the edges in our images, and gives us and outline of our moving objects. A key parameter of findContours is the parameter mode. By setting mode to RETR_EXTERNAL (retrieve external) I was able to grab only the outer most contours. This is necessary because later we will draw bounding boxes around the contours. We do not want to draw contours around, for example, the designs on a T-shirt of a moving pedestrian. Finally, as mentioned above we draw bounding boxes around the contours using the OpenCv function rectangle, and by drawing these rectangles on our originally captured frame we can track our moving objects.
This algorithm yielded fairly successful results on the Android phone. Some pitfalls were that the camera frames would lag due to the amount of processing done on each frame. This could be fixed by fine tuning the number of time erosion and dilation of applied to the frames. Erosion and dilation seemed to take up impacting amounts of processing power. Also, if some form of stabilization were to have been used, the user could move around with the camera while tracking objects and detection/ tracking would not be affected by camera jitter. In the future, I would like to make these improvements to make this project more robust.

Link to project: https://github.com/snoopy7/Android_MovingObjectDetector

note: video of results (outputs) are also included in the repository. However, inputs are not available since data was captured on the fly